Winchcombe Swift Support Group – Acceptability of fitting our M30 design swift boxes on a wall/roof with a southern aspect.

Concern has been expressed that fitting our swift boxes on south facing aspects could lead to excessive temperatures in these swift boxes (compared to say boxes fitted on a northern aspect) that could cause overheating mortality of young swifts. This note sets out to dispel such concerns based on the high reflectance of the ‘white’ roof and the ‘off white’ walls of our M30 designed boxes which minimise radiant heating of south facing boxes compared with north facing boxes. In addition the overhanging roof and the angled front face of the box also ensure that during the peak heating period of the day in June and July (say 10am to 4 pm) the front face of the box remains in shadow and will not be subject to the sun’s radiant heating.

As a result of the information in this note it is concluded that it is perfectly acceptable to fit our swift boxes on a southern aspect.

1. Theoretical calculation of surface temperatures caused by the sun’s radiant heating.

Average annual solar radiation arriving at the top of the earth’s atmosphere is roughly 1361 W/m2. The sun’s rays are attenuated as they pass through the atmosphere, leaving maximum normal surface irradiance at approximately 1000 W/m2 at sea level on a clear day. This irradiance, if impinging on a surface, can heat it up above the ambient air temperature. The crucial issue is how much of the impinging radiation is reflected off the surface. If most of it is reflected off the surface there will be no radiant heat contribution to the surface temperature. If most of it is absorbed there will be significant additional heating above the ambient temperature.

The crucial figure is the reflectance of the surface. Our boxes have shiny white uPVC roofs and painted ‘off white’ front and sides. Various data sources (including Ref 1) suggest we can assume an 80% reflectance for the surface of our boxes. Therefore only 20% of the sun’s radiation will heat up the surface of our box until it reaches a temperature causing out going radiation that balances the absorbed radiation.

1000 x 0.2 = SB x TB4
where SB is the Stefan Boltzmann constant (5.67 x 10-8 W/m2 K4) and TB is the box surface temperature necessary to radiate away the 20% 0f absorbed heat.

The calculation givesTB = 2440K ie -290C which means radiative heat transfer would not contribute to the surface temperature of the box

If the surface had the reflectance of a black body (0%) it would heat up to 364.40K ie 910C which would be clearly significant in heating up the box.

The minimum level of surface reflectance that could potentially cause a surface temperature of concern can also be calculated. If we assume the surface temperature of concern is, say, 300C the minimum reflectance to prevent this occurring must be at least 47.8%. This is easily achieved by the white and ‘off white’ colours of our swift boxes.

Note:
For a southerly aspect swift box the wall on which it is attached will receive radiant heating from the sun as well as convected heat via the ambient air temperature. If there is significant additional radiant heat there could be a concern that heat from the wall surface could conduct to the wall behind the box and from there heat up the box. This is judged unlikely for several reasons:

1. Most of the houses on which we fit boxes are made from Cotswold stone or a concrete mix version of Cotswold stone. There surfaces are very light in colour giving them relatively high reflectance values resulting in temperatures which will be the same or nearly the same as the ambient air temperature causing little or no brick heating above ambient temperature.
2. If the brickwork surrounding the box was at a higher temperature than ambient, the heat would have to conduct itself on a pathway to the back of the box before transferring heat to the back of the box. This is a tortuous path when easier heat transfer routes are available directly into the brickwork.
3. Finally, in general, the surface of Cotswold stone bricks are not flat (in contrast to standard red bricks) meaning that most of the back of a box has an air interface between the box and the brick. This will encourage convection currents at ambient air temperature to circulate at the back of the box, insulating it from higher temperatures in the brickwork.

2. An analysis of box colour and it’s effect on box temperature for different box aspects

A paper has been written (Ref 1) by the Department of Ecology, Environment and Evolution, La Trobe University and the School of BioSciences, the University of Melbourne, both in Victoria, Australia looking at how the colour of artificial nest boxes affects the temperature within these boxes for various different aspects (north, south, east and west). The results from this paper are very relevant to our particular concern and are briefly described here. Interestingly it should be noted that whilst the direction of concern in the UK is south facing, in Australia it is north facing.

The paper investigated how differences in surface reflectance influenced temperature profiles of nest boxes painted three different colours (dark-green, light-green and white: total solar reflectance 5.9%, 64.4% and 90.3% respectively) using boxes designed for three groups of mammals: insectivorous bats, marsupial gliders (most similar to our swift boxes) and bushtail possums (fig 1).

The following is a brief summary of the outcome relevant to our situation:

a) The values given for paint reflectance were measured in the assessment, the value given for white paint, 90.3%, is relevant for our boxes. In the calculation in section 1 a value of 80% was assumed which easily bounds this value.

b) Ref 1, Figure 4 for bat box design indicates that at an ambient temperature of 300C for north facing boxes (equivalent to our south facing boxes) the temperature within the white box was about 20C above ambient whereas that within the dark green box was 100C above ambient which would be very significant for nesting swifts. In the case of glider boxes (a box with a hole cut out on the front face for mammal usage and hence similar to our boxes) Ref 1, figure 6 indicates that with a similar ambient temperature of 300C for their north facing boxes the temperature within the white box was the same as the ambient temperature but the temperature within the dark green box was 50C above ambient. This increase could be of concern for nesting swifts but it is significantly lower than for the bat box design because of the improved convection through the entrance hole which would be the similar for our swift boxes.

It is concluded that the colour of the boxes is very important to the internal temperature reached in the boxes. There is virtually no temperature increase for a white painted box; since our boxes are effectively white it is completely acceptable to site them south facing.

3. The M30 box design ensures that the front face of our swift boxes is in shadow during the hottest part of the day.

The M30 box design is such that the roof extends beyond the front face of the bird box which contains the entrance hole. In addition, the front face of the box slopes backwards from top to bottom. This design coupled with the UK latitude means that for probably the hottest hours during a summer’s day (June and July) between, say, 10 am and 4 pm the front face of the box is in shadow adding to our confidence that it is perfectly acceptable to site our boxes in a south facing direction (see Appendix 1).

Reference 1:
Surface reflectance drives nest box temperature profiles and thermal suitability for target wildlife.
Authors: Stephen R. Griffiths, Jessica A. Rowland, Natalie J. Briscoe, Pia E. Lentini, Kathrine A. Handasyde, Linda F. Lumsden, Kylie A. Robert
Australian publication: dated May 4th 2017

Figure 1 Box types used in Reference 1

Appendix 1: Front face of our M30 box in shadow

Brian Weller	8th October 2024